SNES 2 DB9 Joystick Converter
Description ATtiny84 implementation

# Document history
Date	Version	Responsible	Changes
2020-09-26	V0.2	Arndt	CPU clock configuration changed to 4MHz
2020-09-21	V0.1	Arndt	Initial version

# Table of contents

# Abstract
This document describes the ATtiny84 implementation of the SNES2DB9 converter.
The project is implemented on regular perforated board.
Pin mappings are optimized for direct connection to screw terminals, one GPIO port handles all output signals, one GPIO port handles all input signals.
# Bill of materials
- U1 ATtiny84 microcontroller (14pin DIP)
- screw terminals for DB9 joystick and SNES gamepad connection
- R1 10kOhm pulldown resistor
# Mapping of ATTiny84 controller pins
Refer to the datasheet for further reference.

PDIP pin	Port reference	Pull-up configuration	SNES2DB9 pin reference
1	VCC	---	+5V,power supply from DB9 joystick to ATtiny84 and SNES controller
2-4	PB0,PB1, PB3	---	unused
5	PB2	Internal pull-up	SNES DATA
6	PA7	Internal pull-up	SNES CLOCK
7	PA6	External pull-down R1	SNES LATCH
8-12	PA5-PA1	---	DB9 joystick values () PA5: up PA4: down PA3 left PA2: right PA1: fire
13	PA0	---	unused
14	GND	---	Common ground with DB9 joystick and SNES gamepad

# Schematics
tbd

# Software configuration
- controller uses internal oscillator at 1MHz via fuse, upscaled at runtime to 4MHz via Clock Prescale Register CLKPR
- SNES reader timing derived from a 200µs timer tick
- 16ms time based derived from 200µs timer for DB9 update and autofire generation
- autofire cycletime 16ms