SNES 2 DB9 Joystick Converter
System specification

# Document history
Date	Version	Responsible	Changes
2020-09-20	V0.1	Arndt	Initial version

# Table of contents

# Abstract
SNES2DB9 is a software package to allow implementation of a converter to connect a SNES style gamepad with shift register to a system using the Atari DB9 joystick standard (Atari 2600, C64, Amiga, Atari ST, etc.)

The converter software runs on any microcontroller and uses hardware abstraction.

# Functional blocks

Block type	Description	comment
Red rectangle	Software component	VCC for both microcontroller and SNES gamepad
Grey trapeze	Hardware pin	Widening trapeze indicates output / Narrowing trapeze indicates input

# Hardware requirements
Resistor configuration shall utilize pull-up resistors internal to the microcontroller if possible.
## Atari DB9 joystick connection

Signal	Pin number	Description
+5V		VCC for both microcontroller and SNES gamepad
GND		Common ground for microcontroller and SNES gamepad

## SNES Gamepad connection
Signal	Pin number	Resistor configuration	Description
+5V	1	---	Directly supplied from Atari DB9 joystick
CLOCK	2	Pull-up	Microcontroller output, control pin According to the SNES controller interface protocol, the clock is idle high.
LATCH	3	Pull-down	Microcontroller output, control pin According to the SNES controller interface protocol, the latch is idle low.
DATA	4	---	Microcontroller input, data pin Data is active low according to the SNES interface protocol.
GND	7	---	Common ground connection

# Functional software requirements
### Hardware abstraction
The software abstracts hardware access through user supplied functions.
The functions are called when needed.
The hardware shall immediately change pin states on call of the hardware abstraction.

# Formal software requirements
- The software shall be written in C99.
- Each functional block shall be provided as a seperate source file.