SNES 2 DB9 Joystick Converter
User requirements

# Document history
Date	Version	Responsible	Changes
2020-08-24	V0.1	Arndt	Initial version
2020-09-20	V0.2	Arndt	Add document content heading

# Table of contents

# User stories
ID	Story
S1	„I want to connect an SNES controller to an Atari-style DB9 joystick port for the main directions and a fire button. Power supply shall be possible through the DB9 connector“
S2	„The four main fire buttons on the SNES pad shall be utilized in a sensible fashion.“

# User requirements
In addition to the user stories above the following requirements are defined.

ID	Requirement
R1	The adapter should be small and not exceed 5x7x1cm (WxLxH)
R2	No buttons or switches outside of SNES controller required.
R3	B button on SNES shall be fire button / A button on SNES shall be mapped as “Joystick up”, jump button feature / Y button on SNES shall act as autofire when pressed. / Directional pad on SNES shall map directly to joystick directions.
R4	SNES controller polling every 20ms (50Hz) or faster.